GPU Architectures SS2019
Dominik Schörkhuber & Thomas M. Galla

---
Overview
- Execution and measurement framework
- Dimensions of Optimization
- Implementation variants
- Measurement results
- Summary and takeaways

---
Execution & Measurement Framework
- Automated execution of all algorithm implementations
- Command line configurable
  - sample size, window size, iterations
- Verifying correctness
  - Comparison with Lemire's implmentation
- Measurement of (average) runtime of each algorithm
- Easy to add new algorithm implementations

---
Sample Session
$ ./streaming_min_max_comparison -s 10000000 -w 500 -i 11
Performing a comparison using the following parameters:
  window_size = 500
  sample_size = 10000000
  number_of_iterations = 11
lemire = 2315.039919 milliseconds
cuda plain - cuda malloc = 234.845854 milliseconds
cuda plain - page locked memory = 3055.436376 milliseconds
cuda plain - page locked shared memory = 103.675406 milliseconds
thrust_naive = 221.098370 milliseconds
thrust = 235.481252 milliseconds
cuda plain - cuda tiled = 127.926657 milliseconds

---
Dimensions of Optimization
- CUDA framework
  - Plain CUDA
  - Thrust
- Memory allocation & data transfer
  - Explicit memory allocation and transfer
  - Page-locked host memory
  - Page-locked host memory + shared memory as cache
- Parallelization strategy
  - One thread per sliding window/output value („linear scan“)
  - Binary reduction and tiling („log linear scan“)

---
Explicit Memory Alloc. & Transfer (1)
- cudaMalloc()/cudaFree()/cudaMemcpy()
- Expectation
  - Allocation overhead
  - Memory transfer overhead
  - Memory copy overhead (2x each direction!)

---
Explicit Memory Alloc. & Transfer (2)

---
Page-Locked Host Memory (1)
- cudaHostRegister()/cudaHostDeregister()
- Expectation
  - Allocation overhead eliminated
  - Memory transfer overhead still there
  - Memory copy overhead partly eliminated
    (1 x each direction!)

---
Page-Locked Host Memory (2)
Utterly useless!

---
Page-Locked Host Memory (3)
- Actually a massive deterioration
- Hypothesised causes
  - Lack of possibility to coalesce small memory accesses into single bulk transfer
  - Slow PCI bus
- Interestingly depends strongly on HW platform

---
Page-Locked Host Mem. & Cache (1)
- Use page-locked host memory
- Use shared memory on GPU as program controlled cache
  - Shared memory as fast as L1 cache
  - Program controlled instead of LRU
- Expectation
  - Massive memory access overhead of pure page-locked memory drastically reduced

---
Page-Locked Host Mem. & Cache (2)
- Split computing kernel into two parts
  - Parallelized memory transfer into shared memory
    - Combined effort of all threads of a thread block
  - Actual compuation on shared memory

---
Page-Locked Host Mem. & Cache (3)

---
Linear Scan
- One thread per output
- Incremental computation

---
Log Linear Scan
- Binary reduction
- Combine results

---
Implementation of Algorithms
- CUDA
  - cuda_malloc: malloc – linear scan
  - cuda_pagelocked: page-locked – linear scan
  - cuda_pagelocked_shared: page-locked & shared memory – linear scan
  - cuda_tiled: page-locked & shared memory – log linear scan & tiling
- Thrust
  - thrust_naive: linear scan
  - thrust: log linear scan & tiling

---
Measurements
- Conducted for all algorithm flavors
- For various sample and window sizes
- On two different HW platforms
  - NVIDIA RTX2070
  - NVIDIA Tesla K10.G2

---
Results – NVIDIA RTX 2070
Win: 1000
Samples
Milliseconds
Win: 100
Samples
Milliseconds

---
Results – NVIDIA Tesla K10.G2
Win: 100
Samples
Milliseconds
Win: 1000
Samples
Milliseconds

---
Summary & Takeaways (1)
- Performance of code running on a GPU is influenced by a multitude of factors, thus
  - Know your workload and your HW
  - Measure carefully and optimize
    - If measurement result are inconclusive, measure again …
- Optimization for one HW/workload might be a deterioration on another
  - Consider going for a hybrid solution
    - multiple kernels
    - select appropriate one during run-time (based on HW and workload)

---
Summary & Takeaways (1)
- Performance of code running on a GPU is influenced by a multitude of factors, thus
  - Know your workload and your HW
  - Measure carefully and optimize
    - If measurement result are inconclusive, measure again …
- Optimization for one HW/workload might be a deterioration on another
  - Consider going for a hybrid solution
    - multiple kernels
    - select appropriate one during run-time (based on HW and workload)

---
Summary & Takeaways (2)
- Don‘t be too clever! - a straight forward „naive“ solution might outperform a complex „smart“ solution
- „Premature optimization is
  the root of all evil“
  [Donald Knuth]