GPU Architecture SS2019 - Status
Dominik Schörkhuber & Thomas M. Galla

---
Status Quo
- Github repository created
- Execution and measurement framework created
- Lemire‘s implementation added
- Naive plain CUDA implementation added

---
Demo
1. [tom@herz GPU_Arch_SS19]$ ./streaming_min_max_comparison -s 10000000 -w 5 -i 10
3. Performing a comparison using the following parameters:
4. window_size = 5
5. sample_size = 10000000
6. number_of_iterations = 10
8. lemire = 18.159 seconds
9. cuda plain = 7.2461 seconds
10. thrust = 0.528345 seconds
11. cuda streams = 0.527815 seconds

---
Naive CUDA Implementation Profiling

---
Next Steps (1)
- Performance optimizations for plain CUDA implementation
  - Use page locked memory ranges
    - cudaHostRegister() and cudaHostGetDevicePointer()
  - Use shared memory as program controlled per block cache
    - Explicitly transfer data to and from shared memory by kernel code
  - Schedule the memory transfers in a way to minimize bank conflicts

---
Next Steps (2)
- Add Thrust implementation
- Add CUDA streams implementation